### How to Find Us

Address:	1976 Cherrywood Street
	Vista, CA 92083 USA

Telephone:	760-598-8555

Fax:	760-598-1114

Web:	www.zmc.com

e-mail:	Sales Department ( sales@zmc.com

### Technical Assistance ( support@zmc.com

Industrial design:  Rienhold Weiss Design, Chicago, Illinois

12

Z-Keys™

Z-Keys Desktop and Z-Keys Pro
PS/2 Programmable Keyboards
by
Zak Morris Co., Inc.

| Zak Morris Co., Inc. 1976 Cherrywood Street Vista, CA 92083 USA | 760-598-8555 FAX 760-598-1114 e-mail: info@zmc.com WWW: http://www,zmc.com |
| --- | --- |

Z-Keys Pro and Z-Keys Desktop Programmable Keyboards

Z-Keys Pro (58 keys) and Z-Keys Desktop (20 keys) are fully programmable keyboards. Each key on the Z-Keys accepts multiple keystrokes and/or keyboard combinations and you can customize Z-Keys to work with a dedicated application or multiple programs and/or platforms. A switch activates program mode that allows the user to program each key independently. In addition, the board supports two layers of commands, which means that two sets of keystrokes can be assigned to each key (almost doubling the number of programmable keys!), and any key on the Z-Keys can be the one that toggles between layers.

Z-Keys are easy to program, and they work alongside standard keyboards or as standalone keyboards. In other words, both the Z-Keys and the standard keyboard can send keyboard codes to the computer, or the Z-Keys can operate as the only keyboard attached to the computer. If both keyboards are used, switching between the devices is instantaneous, because of Y-mouse technology that makes the switching operation invisible to the user. The keyboards actually appear to send keyboard signals to the computer at the same time. Whether you use it for a single application or all your most-used programs, you’ll be sure to appreciate the easy programming, flexibility and time saving features of the Z-Keys.

# Installing Your Z-Keys Pro or Z-Keys Desktop Programmable Keyboard

Turn off the computer.

- Make the Z-Keys compatible with your computer by attaching the keyboard connector to one of the ends of the Z-Keys cord – either to make it a large 5-pin or a small 6-pin PS/2 connector, whichever works for your computer.

- Plug the Z-Keys connector (the end with the pins) into the keyboard port on the computer.

- Plug the regular keyboard into the other end of the Z-Keys cord.
NOTE:  The regular keyboard is not required for the Z-Keys to operate, but it is required for programming the Z-Keys.

- Turn on the computer and make sure the standard keyboard operates properly after complete boot-up. Check that the top light is on to make sure the Z-Keys installed properly.

2

### LIMITED WARRANTY

For all Z-Keys products purchased and installed in the United States and Canada, Zak Morris Co., Inc. (ZMC) warrants that the Z-Keys product will be free from defects in materials and workmanship under normal use and service, and will meet the specifications presented by ZMC at the time of original purchase, for one year as evidenced by a copy of the purchase receipt.  Under this warranty, ZMC will, at its sole option, repair or replace any Z-Keys product which is defective, provided that you are responsible for (i) the cost of transportation of the product to ZMC or its designated service facility, and (ii) any loss or damage to the product resulting from such transportation.

Upon discovery of a defect in the product within the Warranty Period, you should notify ZMC Technical Support via telephone to obtain an RMA (return authorization number) and instructions for shipping the product to a service location designated by ZMC.  You should send the product, shipping charges prepaid, to the designated location, accompanied by the return authorization number, your name, address, and telephone number, proof of purchase, and a description of the defect.  ZMC will pay for return of product(s) to the customer.

ZMC shall have no responsibility to repair or replace the Z-Keys product if the failure has resulted from accident, abuse, mutilation, misuse, or repair/modification performed by any entity other than ZMC.

THIS WARRANTY IS EXCLUSIVE OF ALL OTHER WARRANTIES, WHETHER EXPRESSED, IMPLIED, OR STATUTORY.  ZMCDOES NOT WARRANT
THIS Z-Keys PRODUCT FOR FITNESS FOR A PARTICULAR PURPOSE OR MERCHANTABILITY.  ZMCAND ITS EMPLOYEES SHALL NOT BE HELD LIABLE FOR ANY CONSEQUENTIAL, INDIRECT, OR INCIDENTAL DAMAGES, EVEN IF ADVISED OF THEIR POSSIBILITY, ARISING OUT OF THE USE OR INABILITY TO USE THIS PRODUCT.  SOME STATES DO NOT ALLOW FOR THE EXCLUSION OR LIMITATION OF CERTAIN LIABILITIES, SO THE ABOVE LIMITATIONS MAY NOT APPLY TO YOU.  THIS WARRANTY GIVES YOU SPECIFIC LEGAL RIGHTS, AND YOU MAY ALSO HAVE OTHER LEGAL RIGHTS WHICH VARY FROM STATE TO STATE.

In the event that the above limitations are held unenforceable, ZMC’s liability for any damages to you or to any party shall not exceed the purchase price you paid, regardless of the form of any claim.

This limited warranty is valid for and only applies to products purchased and used inside the United States (and its territories) and Canada.

This limited warranty is governed by the laws of the United States of America and the state of California.

© 1998-2002 Zak Morris Co., Inc.  All rights reserved.

Z-Keys is a trademark of Zak Morris Co., Inc.  PS/2 is a registered trademark of International Business Machines, Inc.  All other trademarks are property of their respective owners.

11

#### Horizontal and Vertical Double-keys:

Horizontal and/or vertical double-keys can replace two single keys. Remove the single key with the key-puller that comes with the Z-Keys by positioning the key-puller teeth under the key and pulling straight up on the key cap. Press the double-key in place over the two exposed switch stems. NOTE:  If the individual keys were programmed before, erase both before installing a double-key.

## Box Contents	Additional Accessories*

| Z-Keys Pro or Z-Keys Desktop Two vertical double-keys One horizontal double-key One key-puller One keyboard connector Instruction manual and (for some versions) a diskette | Basic Accessory Pack: Two vertical double-keys One horizontal double-key One key-puller Vertical Keys Pack: 10 vertical double-keys Horizontal Keys Pack: 10 horizontal double-keys Single Keys Pack: 10 single keys *Available directly from ZMC |
| --- | --- |

## FCC Declaration of Conformity

This device complies with Part 15 of the FCC rules.  Operation is subject to the following two conditions:  (1) This device may not cause harmful interference, and
(2) this device must accept any interference received, including interference
that may cause undesired operation.

This equipment has been tested and found to comply with the limits for a Class B digital device, pursuant to part 15 of the FCC rules.  These limits are designed to provide reasonable protection against harmful interference when the equipment is operated in a residential installation.  This equipment generates, uses, and can radiate radio frequency energy and if not installed and used in accordance with the instruction manual may cause harmful interference to radio communications.  However, there is no guarantee that interference will not occur in a particular installation.  If this equipment does cause harmful interference to radio or television reception, which can be determined by turning the equipment off and on, the user in encouraged to try to correct the interference by one or more of the following measures:

- Reorient or relocate the receiving antenna.

- Increase the separation between the equipment and the receiver.

- Connect the equipment into an outlet on a circuit different from that to which the receiver is connected.

- Consult the dealer or an experienced radio TV technician for help.

Any changes or modifications not expressly approved by the manufacturer could void the user’s authority to operate the equipment.

10

# Programming Your Z-Keys Pro or Z-Keys Desktop Keyboard

NOTE:  Basic programming instructions are on the back of the Z-Keys.

- In order to program the Z-Keys the standard keyboard must be attached to the computer along with the Z-Keys, so, install the Z-Keys between the computer and the main keyboard as described in the installation instructions above. If the Z-Keys will be a standalone keyboard, remove the standard keyboard after programming is complete.

- It is a good idea to open the application(s) that will use the programmed keys – this makes it easy to test the keys during and after programming.

- Slide the program switch on the Z-Keys up to the program position (a red indicator will be visible to the left of the switch).  NOTE:  The Num, Caps and Scroll Lock lights on the standard keyboard will sequentially blink.

- Tap the key on the Z-Keys that you want to program.  NOTE:  The Num, Caps and Scroll Lock lights will stop blinking and stay on.

- Type (on the main keyboard) the key sequence and/or key combination to program into the key on the Z-Keys. During programming, the monitor will display any alphanumeric keys typed or if you are entering commands the application will perform the function(s) entered.

- When the sequence is complete, tap the key on the Z-Keys again. NOTE: As in step 3, the Num, Caps and Scroll Lock lights on the standard keyboard will sequentially blink. This happens whenever the Z-Keys is in program mode, but no key is currently selected for programming.

- Repeat steps 4, 5 and 6 to program the rest of the keys on the Z-Keys. If you make a mistake on a key, tap it once to stop the programming and then tap it again (step 4) and re-program it with the correct keystrokes.

- When programming is complete, slide the program switch down to the run position. The Z-Keys is ready to use. Enjoy!

NOTE:  When the Z-Keys is in program mode and a no key is being programmed (when the Num, Caps and Scroll Lock lights on the standard keyboard are sequentially blinking) the main keyboard will not work. In addition, the Z-Keys must be in run mode (with the program switch in the down position) for the standard keyboard to work properly.

### Operation

Use the regular keyboard and the Z-Keys at any time. The Z-Keys will automatically send the commands to the computer from the device in use.  NOTE:  The Z-Keys will not boot-up the computer in programming mode.

3

# Additional Instructions for Special Programming Features

In addition to saving keystrokes, you may be interested in additional Z-Keys features like programming different layers, making repeating keys, and erasing keys. The numbers in parenthesis following most of the feature names refer to their numbers on a reference list that follows the descriptions. The first features (1-5) refer to single key programming and the rest (6-10) affect the entire keyboard.

### Single Key Special Programming Features

#### Programming a Layer-toggle Key (1):

To switch to another layer one key must be a dedicated layer-toggle key. This may be any key including a double key, but program it before programming the second layer. To program a layer-toggle key:

- If the Z-Keys is not already in program mode slide the program switch up to the program position.

- Tap the key on the Z-Keys that you want to program.

- Press and hold the <Esc> key on the main keyboard.

- While holding down the <Esc> key, tap the <2> (two) key on the alphanumeric section of the main keyboard (above the Q).

- Release the <Esc> key.

- The lights on the main keyboard will begin to scroll which confirms that the command was accepted.

- If programming the rest of the first layer is complete, slide the program switch to the down or run position.

#### To Program a Second Layer:

- After programming a layer-toggle key, change to the second layer by tapping the layer-toggle key. The Z-Keys must be in run mode, not program mode, when changing to the second layer. The indicator LED on the Z-Keys will change from the top to the bottom light.

- Slide the program switch up to the program position.

- Continue to program this layer as described on page 3, but do not reprogram the layer-toggle key or you will not be able to access the second layer.

4

### Special Programming Features Table

Once you become familiar with the previously described special programming features, the following list of keystrokes may be a useful reference.

## Command Symbol Legend

( indicates when to press and hold a key down

( indicates when to tap a key

( indicates when to release the key.

NOTE:  Numbers between chevrons (<>) are on the alphanumeric section of the keyboard not the number pad.

| Single Key Programming Features |
| --- |
| Feature | Associated Keystrokes |
| 1) Layer-toggle | (<Esc> (<2> (<Esc> |
| 2) Layer-shift | (<Esc> (<1> (<Esc> |
| 3) Repeating Key | (<Esc> (<Left-Shift> (<Esc> |
| 4) Separate Press and Release | (<Esc> (<Left Ctrl> (<Esc> |
| 5) Erasing a Key | (<Esc> (<Esc> (<Esc> |
| 6) Add 0.5 sec. Pause | (<Esc> (<5> (<Esc> |
| Entire Keyboard Programming Features |
| Feature | Associated Keystrokes |
| 6) Slow Transmission Speed | (<Esc> (<3> (<Esc> |
| 7) Normal Speed | (<Esc> (<4> (<Esc> |
| 8) Caps Lock/Unlock Memory | (<Esc> (<8> (<Esc> |
| 9) Caps Lock/Shift Unlock Memory | (<Esc> (<9> (<Esc> |
| 10) No Caps Lock Memory | (<Esc> (<7> (<Esc> |

9

#### No Caps Lock Memory (10):

No Caps Lock Memory is the default for the Z-Keys. If you programmed the Z-Keys with either of the two previous features (8 or 9) and you want to return to the default state:

- While in program mode, tap any key on the Z-Keys.  NOTE:  If the key was programmed before, it will need to be re-programmed after no caps lock memory is programmed.

- Press and hold the <Esc> key on the main keyboard.

- While holding down the <Esc> key, tap the <7> key on the alphanumeric section of the main keyboard (above the E).

- Release the <Esc> key.

- The lights on the main keyboard will begin to scroll which confirms that the command was accepted.

- If programming the rest of the keyboard is complete, return the program switch to the down or run position.

#### Programming Errors:

- If the Z-Keys encounters programming errors, the keyboard LEDs will blink simultaneously on and off.  Turn the programming switch off and back on to reset the Z-Keys to programming mode.

- Errors can occur if:

- There is an unreliable cable connection, check all cords for proper connection.

- The computer is not operating in a mode to accept the entered keys (for example, pressing <Ctrl>, <Alt> and <Delete> may cause a computer reboot and the Z-Keys will not boot-up in programming mode).

- Although unlikely, it is possible to type too many keystrokes into the Z-Keys. If you think that too many commands were entered, retry with a shorter key sequence.

8

#### Programming a Layer-shift Key (2):

To switch temporarily to another layer, program a key as a layer-shift key. A layer-shift key works like the Shift key on the standard keyboard, which you hold down to type capital letters. In the case of the Z-Keys, you hold down the layer-shift key to use the upper-level of keys. The layer-shift key may be any key including a double key. If you wish to use the second layer only with a layer-shift key, rather than a layer-toggle key, change the layer-toggle key to a layer-shift key after programming the second layer. To program a layer-shift key:

- If the Z-Keys is not already in program mode, slide the program switch up to the program position.

- Tap the key on the Z-Keys that you want to program.

- Press and hold the <Esc> key on the main keyboard.

- While holding down the <Esc> key, tap the <1> key on the alphanumeric section of the main keyboard (above the Q).

- Release the <Esc> key.

- The lights on the main keyboard will begin to scroll which confirms that the command was accepted.

- If programming the rest of the first layer is complete, return the program switch to the down or run position.

#### Repeating Keys (3):

Keys on the Z-Keys are not automatically repeating keys, but it’s easy to program them to repeat like the alphanumeric keys on the standard keyboard. To make a key a repeating (typematic) key, hold down <Esc>, tap the <left-shift> key, and release <Esc> before entering the actual text or sequence for that key.

#### Separate Press and Release Commands (4):

The Z-Keys can generate one command when a key is pressed and another when released. For example, a key could type <A> when pressed and <B> when released. A key can also repeat the same function, such as <Ctrl+B> both when pressed and released – this is useful, in this example, as an on and off bold key in programs such Microsoft Word. To program this feature:

- While the Z-Keys is in program mode, tap the key to program.

- Type the keys on the standard keyboard to send to the computer when the operator presses the key down.

- Press and hold the <Esc> key on the standard keyboard.

- While holding down <Esc>, tap the <Ctrl> key.

- Release the <Esc> key.

- Type the keys to send to the computer when the operator releases the key. NOTE:  A maximum of three keystrokes will send on the key release.

5

#### Erasing a Key (5):

Reprogramming a key on the Z-Keys automatically erases the previously saved keystrokes. To erase a key and leave it blank, press the <Esc> key three times during programming.

### Entire Keyboard Special Programming Features

The rest of the features (6-10) affect the entire keyboard and include changing the transmission speed and changing the Caps Lock memory.

#### Slow Transmission Speed (6):

Some applications or systems have a slower response time and the default Z-Keys speed is too fast. To slow the rate at which the Z-Keys sends key commands:

- While in program mode, tap any key on the Z-Keys.  NOTE:  If you saved keystrokes on the key before, it will need to be re-programmed after entering the Slow Transmission Speed command.

- Press and hold the <Esc> key on the main keyboard.

- While holding down the <Esc> key, tap the <3> key on the alphanumeric section of the main keyboard (above the E).

- Release the <Esc> key.

- The lights on the main keyboard will begin to scroll which confirms that the command was accepted.

- If programming the keyboard is complete, return the program switch to the down or run position.

#### Normal Transmission Speed (7):

Normal Transmission Speed is the default for the Z-Keys. If you previously programmed Slow Transmission Speed and you want to return the Z-Keys to the default Normal Transmission Speed:

- While in program mode, tap any key on the Z-Keys.  NOTE: If you saved keystrokes on the key before, it will need to be re-programmed after entering the Normal Transmission Speed command.

- Press and hold the <Esc> key on the main keyboard.

- While holding down the <Esc> key, tap the <4> key on the alphanumeric section of the main keyboard (above the R).

- Release the <Esc> key.

- The lights on the main keyboard will begin to scroll which confirms that the command was accepted.

- If programming the keyboard is complete, return the program switch to the down or run position.

6

### Caps Lock Special Programming Features

The next three features (8-10) affect how the Z-Keys recognizes Caps Lock and Unlock. The first two are specific to certain languages (i.e., English, French, etc.). These features enable the Z-Keys to remember whether Caps Lock was on when saving keystrokes, which frees the user from having to pay attention to the current mode of the standard keyboard when using the Z-Keys. Caps Lock/ Unlock Memory and Caps Lock/Shift Unlock Memory are useful if you want to save keystrokes that are case sensitive (like names and addresses). It is best to program a Caps Lock feature before programming the rest of the Z-Keys.

#### Caps Lock/Unlock Memory (8):

Caps Lock/Unlock Memory works in languages (such as United States English, Latin American Spanish, etc.) that use the Caps Lock key both to turn Caps Lock on and off. To program Caps Lock/Unlock Memory:

- While in program mode, tap any key on the Z-Keys. NOTE:  If you want to save keystrokes on this key, program it after entering the Caps Lock/ Unlock Memory command.

- Press and hold the <Esc> key on the main keyboard.

- While holding down the <Esc> key, tap the <8> key on the alphanumeric section of the main keyboard (above the U).

- Release the <Esc> key.

- The lights on the main keyboard will begin to scroll which confirms that the command was accepted.

- The Z-Keys is now ready to program.

#### Caps Lock/Shift Unlock Memory (9):

Caps Lock/Shift Unlock Memory is for languages (German, French, etc.) that use the Caps Lock key to turn Caps Lock on and the shift key to turn Caps Lock off. To program Caps Lock/Shift Unlock Memory:

- While in program mode, tap any key on the Z-Keys. NOTE: If you want to save keystrokes on this key, program it after entering the Caps Lock/Shift Unlock Memory command.

- Press and hold the <Esc> key on the main keyboard.

- While holding down the <Esc> key, tap the <9> key on the alphanumeric section of the main keyboard (above the I).

- Release the <Esc> key.

- The lights on the main keyboard will begin to scroll which confirms that the command was accepted.

- The Z-Keys is now ready to program.

7